## Slide 1: CMIP compliant processing with CDO
cdo cmor operator

## Slide 2
CMOR Climate Model Output Rewriter
Why use CMOR to create CMIP standard?
Why integrate CDO with CMOR?
CMOR ensures that output has CMIP standard
Different CMIP standards can be produced
Use synergies, avoid repeating work

## Slide 3
Motivation
Why use CMOR to create CMIP standard?
Why integrate CDO with CMOR?
Use the power of CDOs…
  CDO is a well known tool with an active support
  Different infile formats are possible
  Different infile structures can be appropriately processed because CDI enables access to all infile information.

## Slide 4
Motivation
Why use CMOR to create CMIP standard?
Why integrate CDO with CMOR?
cmor_setup(param);
cmor_dataset_json(param);
cmor_load_table(param);
cmor_set_table(param);
cmor_axis(param);
cmor_grid(param);
cmor_set_grid_mapping();
cmor_time_varying_grid_coordinate();
cmor_zfactor()
cmor_variable(param);
cmor_set_deflate();
cmor_set_variable_attribute();
cmor_create_output_path();
cmor_write(param);
cmor_close(param);
…to simplify CMOR:
are included by one cdo cmor operator

## Slide 5
CDI can distinguish between grid types and vertical axes types. The operator calls the appropriate CMOR function by exploiting this information.  ‚Hard code‘ is reduced and processable infile types are enlarged
Required but missing information can be detected and, in some cases, can be automatically computed like grid point bounds or relative time axis values  Postprocessing by user is reduced.
height
pressure
Advantages
1970-01-01
1970-01-02
1970-01-03
1970-01-04
Days since 1970-01-01
0
1
2
3

## Slide 6
Tests and applications
cdo cmor with CMOR2
Tested for MPIESM-1 versions for
Applied at least
cdo cmor with CMOR3
Tested for MPIESM-1-2-HR
Amip
In Karlsruhe Institute of Technology (KIT)
For HAPPI at DKRZ
For paleo data at the MPI
piCtrl
historical
For historical
Also tested CMOR2 with CORDEX compliant data

## Slide 7
Support
Extra documentation within CDOs
Hands-on, will also be available on youtube
Active user support via cdo support
Visiting institutes for workshops on demand

## Slide 8
Development of the cdo cmor Operator for producing CMIP compliant output
Project depen-dent check of attributes
Mapping of variables
Auxillary variables and bounds calculation
Append-Mode
Components

## Slide 9
cdo cmor,cmip6_mip_tables_325/CMIP6_Amon.json,i=infotable.txt,mt=mapping_table.txt test.nc
„variable_entry“:{
„ccb“: {
„frequency“: „mon“,
„modeling_realm“:“atmos“,
MIP-Table
institude_id=MPI-M
source_id=MPIESM-1-2-HR
experiment_id=historical
realization_index=1
physics_index=1
initialization_index=1
forcing_index=1
activity_id=CMIP6
&parameter cmor_name=clt c=164 units="1“ cm="m" /
&parameter cmor_name=uas c=165 units="m s-1" cm="m" /
&parameter cmor_name=vas c=166 units="m s-1" cm="m" /
&parameter cmor_name=tas c=167 units="K“ cm="m" /
Info table
Mapping table

## Slide 10
Mapping Line selection
The mapping table is read in line by line
Line which contains a matching cmor_name is identified
Line which contains a matching name or code is identified
If matches with parameter one, line is applied. Else, it is denied.
Line is saved, others are tested. The last line with matching cmor_name is applied.
cmor_name is specified in the command line?
project_mip_table in identified line?
A cmor variable is the uniqe combination of cmor_name and project_mip_table

## Slide 11
Mapping variable selection
Infile variables are read variable by variable
Variable with a matching name or code is slected
name or code is specified in command line?
name or code is specified in mapping table?
Variable with a matching name or code is slected
Line is denied

## Slide 12
As long as the data request changes, CMOR3 subversion changes
Data request tables of earlier versions are not compatible with recent CMOR3 subversions (No downward compatibility)
Versions of cdo cmor with CMOR3 are only compatible with a corresponding data request version, today only with the recent version
Right now, CMOR3 still needs updates because an important feature (append mode) will be in the next update and, sometimes, it causes unpredictable behavior
CMOR3 development stage

## Slide 13
New grid information required: grid_label, nominal_resolution
New outfile template with version nr. What if data is appended?
Renamed and restructured values of product and source which makes downward compatibility difficult
A tool to create a cdocmorinfo file is provided at https://c6dreq.dkrz.de/cdocmorinfo
Changes in the Metadata standard in CMIP6

## Slide 14
New tables and new cmor names for cmor variables make it difficult to link CMIP5 variables to CMIP6 variables
Different CMOR labels for different vertical axes in one MIP-table  New keyword z_axis
New cell_method diurnal cycle
Two Character axes for one variable  Processing in progress
Changes in the data standard in CMIP6

## Slide 15
CMOR2
  produces CMIP5 and CORDEX standard:
  Static metadata requirement
  Static outfile template
  Append mode not applicable for hybrid vertical axes
CMOR3
  Produces CMIP6 standard
  MIP-Tables in JSON format
  Metadata requirements only defined by project
Differences in CMOR versions

## Slide 16
Postprocessing like temporal aggregation and diagnostics needs to be performed before calling the operator
Operator chaining can avoid producing lot of in- and output
Limits

## Slide 17
Other experiments/MIPs request variables formatted with special cmor labels which needs to be integrated if the operator should be used for these too:
  Special antarctic/greenland grids
  MORE?
Adaptions to request updates needs to be done ( 2 char axes, diurnal cycle )
Enable downward compatibility? <-> Produce CMIP5 data with CMOR3?
  Either by using CMIP6 request and adding missing global attributes
     Some variables cannot be CMIP5 compliant when its request changes
  Or by creating MIP-tables in json format for CMIP5
Outlook

## Slide 18: Thank you!
Questions at: